## Slide 1: EE227 – Digital Logic Design
Lecture 12

## Slide 2: Outline
Exclusive OR (XOR) Function
Parity Generation and Checking
Quiz 2 Solution
Mid Term I Solution and Result

## Slide 3: Exclusive OR Function (XOR)
The Exclusive-OR (XOR) is denoted by  and performs the following logical operation
A  B = AB’ + A’B
Exclusive NOR is complement of XOR
The following identities are true for XOR
A  0 = A A  1 = A’ A  A = 0
A  A’ = 1 A  B’ = A’  B = (A  B)’
The XOR operation is commutative and Associative
A  B = B  A
(A  B)  C = A  (B  C) = A  B  C

## Slide 4: XOR with NAND Gates

## Slide 5: XOR is an Odd Function
The output of XOR is equal to 1 if an odd number of inputs are equal to 1
For 2 inputs
A  B = AB’ + A’B = (1, 2)
For 3 inputs
  A  B  C = (AB’ + A’B)C’ + (AB + A’B’)C
  = AB’C’ + A’BC’ + ABC + A’B’C
  = (1, 2, 4, 7)
For 4 inputs
A  B  C  D = (AB’ + A’B)  (CD’ + C’D)
  = (AB’ + A’B)(CD + C’D’) + (AB + A’B’)(CD’ + C’D)
  = (1, 2, 4, 7, 8, 11, 13, 14)

## Slide 6: Even Function
The complement of XOR is an even function
  For 2 inputs
    (A  B)’
  For 3 inputs
    (A  B  C)’
  For 4 inputs
    (A  B  C  D)’

## Slide 7: Practice Problem 1
Construct the circuit diagram for 4 input odd function

## Slide 8: Parity Generation and Checking
Exclusive-OR functions are very useful in systems requiring error detection and correction codes
This is done with the help of a parity bit
  The parity bit is an extra bit added to the original message to make the number of 1’s even or odd
  Parity bit is added at MSB position
  For example the message 011 0010 will be written as
    1011 0010 with even parity and
    0011 0010 with odd parity
The circuit that generates the parity bit in the transmitter is called a parity generator
The circuit that checks the parity in the receiver is called a parity checker

## Slide 9: Parity Generator and Checker (1/3)
x,y, and z are inputs
For even parity the number of 1’s including Parity bit (P) must be even
P = x  y  z
For parity checker the inputs are x, y, z, and P and the output is 1 if the number of 1’s are odd, which means that an error has occurred
C = x  y  z  P

## Slide 10: Parity Generator and Checker (2/3)

## Slide 11: Parity Generator and Checker (3/3)
The parity generator can be implemented with the circuit of parity checker
This can be done by connecting the input P with the logic 0 and marking the output as P

## Slide 12: Practice Problem 2
Modify the circuit of 4 bit parity checker to convert it to a 3 bit even parity generator

## Slide 13: Quiz 2
Solution

## Slide 14: Quiz 2 (Paper A)
Question Number 1
Prove the following Boolean equation using Boolean algebra:
xyz’ + x’yz’ + xy’z’ + x’y’z’ + z = 1

## Slide 15: Quiz 2 (Paper A)
Question Number 2
Write the Boolean equation (in simplified form) and draw the logic diagram of the circuit whose output is defined by the following truth table.
Hint: Use minterms or maxterms

## Slide 16: Quiz 2 (Paper B)
Question Number 1
Reduce the following Boolean expression to one literal.
A’B(D’ + C’D) + B(A + A’CD)

## Slide 17: Quiz 2 (Paper B)
Question Number 2
For the given circuit, write the equivalent Boolean expression and construct the truth table

## Slide 18: Mid Term I
Solution
Was Done in Class