## Slide 1: EE227 – Digital Logic Design
Lecture 6 – 8

## Slide 2: Outline
Boolean Algebra
Boolean Functions
Canonical Forms
  Minterms and Maxterms
Standard forms
  Sum of Products (SOP)
  Product of Sums (POS)
Digital Logic Gates
Integrated Circuits
Quiz 1 Solution

## Slide 3: Basic Definitions (1/2)
Boolean algebra, like any other deductive mathematical system, may be defined with a set of elements, a set of operators, and a number of unproved axioms
Set
  A set of elements is any collection of objects, usually having a common property
  If S is a set, and x and y are certain objects, then the notation x  S means that x is a member of the set S and y  S means that y is not an element of S
  A set with a denumerable number of elements is specified by braces: A = {1, 2, 3, 4}

## Slide 4: Basic Definitions (2/2)
Binary Operator
  A binary operator defined on a set S of elements is a rule that assigns, to each pair of elements from S, a unique element from S
  As an example, consider the relation a *b = c
  We say that * is a binary operator if it specifies a rule for finding c from the pair (a, b) and also if a, b, c  S
  However, * is not a binary operator if a, b  S, and if c  S

## Slide 5: The Postulates of a Mathematical System
Closure
  A set is said to be closed if the result obtained after applying a binary operator belongs to the same set
Associative Law
  (x * y) * z = x * (y * z) for all x, y, z,  S
Commutative Law
  (x * y) = (y * x) for all x, y,  S
Identity Element
  e * x = x * e = x for every x  S
Inverse
  x * y = e (y is inverse and e is identity element)
Distributive Law
  x * (y . z) = (x * y) . (x * z)

## Slide 6: Axiomatic Definition of Boolean Algebra (1/2)
In 1854, George Boole developed an algebraic system now called Boolean algebra
In 1938, Claude E. Shannon introduced a two‐valued Boolean algebra called switching algebra that represented the properties of bistable electrical switching circuits
We will discuss the two valued Boolean algebra only

## Slide 7: Axiomatic Definition of Boolean Algebra (2/2)
Boolean algebra is an algebraic structure defined by a set of elements, B, together with two binary operators, + and . , provided that the following (Huntington) postulates are satisfied
  The structure is closed with respect to + and .
  The elements 0 and 1 are identity elements w.r.t + and . Respectively
  The structure is commutative w.r.t + and .
  The operator . is distributive over + and the operator + is distributive over .
  For every x  B there exists x’  B such that x + x’ = 1 and x.x’ = 0
  There exist at least two elements x, y  B such that x ≠ y

## Slide 8: Two Valued Boolean Algebra
A two‐valued Boolean algebra is defined on a set of two elements, B = {0, 1}, with rules for the two binary operators + and . and complement as shown in the following operator tables
These rules are exactly the same as the AND, OR, and NOT operations, respectively

## Slide 9: Practice Problem 1
Show that the Huntington postulates are valid for the set B = {0, 1} and the two binary operators + and .
Huntington postulates are:
  The structure is closed with respect to + and .
  The elements 0 and 1 are identity elements w.r.t + and . Respectively
  The structure is commutative w.r.t + and .
  The operator . is distributive over + and the operator + is distributive over .
  For every x  B there exists x’  B such that x + x’ = 1 and x.x’ = 0
  There exist at least two elements x, y  B such that x ≠ y

## Slide 10: Basic Theorems and Properties of Boolean Algebra (1/2)
Duality
  It states that every algebraic expression deducible from the postulates of Boolean algebra remains valid if the operators and identity elements are interchanged
  If the dual of an algebraic expression is desired, we simply interchange OR and AND operators and replace 1’s by 0’s and 0’s by 1’s

## Slide 11: Basic Theorems and Properties of Boolean Algebra (2/2)

## Slide 12: Practice Problem 2
Prove the followings
  x + x = x
  x . x = x
  x + 1 = 1
  x . 0 = 0
  x + xy = x
  x(x + y) = x
  (x + y)’ = x’y’

## Slide 13: Operator Precedence
The operator precedence for evaluating Boolean expressions
  Parentheses
  NOT
  AND
  OR

## Slide 14: Boolean Functions (1/2)
A Boolean function described by an algebraic expression consists of binary variables, the constants 0 and 1, and the logic operation symbols
F1 = x + y’z
A Boolean function can be represented in a truth table
The number of rows in the truth table is 2n, where n is the number of variables in the function
A Boolean function can be transformed from an algebraic expression into a circuit diagram (also called schematic) composed of logic gates connected in a particular structure

## Slide 15: Boolean Functions (2/2)
F1 = x + y’z

## Slide 16: Practice Problem 3
Construct the truth table and circuit diagram for the following Boolean function
F2 = x’y’z + x’yz + xy’

## Slide 17: Algebraic Manipulation (1/2)
When a Boolean expression is implemented with logic gates, each term requires a gate and each variable within the term designates an input to the gate
We define a literal to be a single variable within a term
The function F2 = x’y’z + x’yz + xy’ has 3 terms and 8 literals
By reducing the number of terms, the number of literals, or both in a Boolean expression, it is often possible to obtain a simpler circuit
The manipulation of Boolean algebra consists mostly of reducing an expression for the purpose of obtaining a simpler circuit

## Slide 18: Algebraic Manipulation (2/2)
The simple manipulation consists of applying basic theorems and relations
The function F2 = x’y’z + x’yz + xy’ can be simplified in the following way
  F2 = x’y’z + x’yz + xy’
  F2 = x’z(y’ + y) + xy’
  F2 = x’z(1) + xy’
  F2 = x’z + xy’
The same function is reduced to two terms. The truth table will be the same and the schematic is now simplified

## Slide 19: Practice Problem 4
Simplify the following Boolean functions to a minimum number of literals. Also construct their truth tables and schematics
  x(x’ + y)
  x + x’y
  (x + y)(x + y’)
  xy + x’z + yz
  (x + y)(x’ + z)(y + z)

## Slide 20: Complement of a Function
The complement of a function F is F’ and can be obtained by an interchange of 1’s for 0’s and 0’s for 1’s in the value of the function
The complement of a function may be derived algebraically through DeMorgan’s theorems
DeMorgan’s theorems for any number of variables resemble the two‐variable case
(A + B + C + … + F)’ = A’B’C’… F’
(ABC … F)’ = A’ + B’ + C’ + … + F’
The complement of a function is obtained by interchanging AND and OR operators and complementing each literal

## Slide 21: Practice Problem 5
Find the complements of the following functions by applying Demorgan’s laws
  F1 = x’yz’ + x’y’z
  F2 = x(y’z’ + yz)

## Slide 22: Another Way to Compute the Complement of a Boolean Function
A simpler procedure for deriving the complement of a function is to take the dual of the function and complement each literal

## Slide 23: Practice Problem 6
Find the complements of the following functions by using duality
  F1 = x’yz’ + x’y’z
  F2 = x(y’z’ + yz)

## Slide 24: Canonical Form
Boolean functions expressed as a sum of minterms or product of maxterms are said to be in canonical form
Minterms
  The AND of N variables such that they equals to 1 is called minterm or standard product
  There are 2N possible minterms with N variables
  Minterms are denoted by lower case m
Maxterms
  The OR of N variables such that the result is equal to 0 is called maxterm or standard sum
  There are 2N possible minterms with N variables
  Maxterms are denoted by upper case M

## Slide 25: Calculating Minterms and Maxterms
Each minterm is obtained from an AND term of the n variables, with each variable being primed if the corresponding bit of the binary number is a 0 and unprimed if a 1
Each maxterm is obtained from an OR term of the n variables, with each variable being unprimed if the corresponding bit is a 0 and primed if a 1
The complement of a minterm is equal to its corresponding maxterm

## Slide 26: Minterms and Maxterms for 3 Variables

## Slide 27: Representing a Boolean Function in Canonical Form
Boolean function can be represented in canonical form in two ways
  As a sum of minterms
  As a product of maxterms
To represent a Boolean function in canonical form all the terms of that function must contain all the variables

## Slide 28: Boolean Function in Minterms
Derive the minterms mathematically
  Introduce all the variables in each term by applying postulates/theorems of Boolean Algebra
  Then form the minterms
Collect the minterms from truth table
  Generate the truth table directly from the given function
  Collect the minterms from the truth table

## Slide 29: Practice Problem 7
Express the function F = A + B’C as a sum of minterms

## Slide 30: Boolean Function in Maxterms
Derive the maxterms mathematically
  First convert the function into OR terms
  Introduce all the variables in each term by applying postulates/theorems of Boolean Algebra
  Then form the maxterms
Collect the maxterms from truth table
  Generate the truth table directly from the given function
  Collect the maxterms from the truth table

## Slide 31: Practice Problem 8
Express the Boolean function F = xy + x’z as a product of maxterms

## Slide 32: Standard Forms
The canonical forms are seldom used
The two standard forms to represent Boolean functions are:
  Sum of Products (SOP)
    Each term is a sum of 1 or more literals
    All the terms are combined with AND
    F1 = y’ + xy + x’yz’
  Product of Sums (POS)
    Each term is a product of 1 or more literals
    All the terms are combined with OR
    F2 = x(y’ + z)(x’ + y + z’)
The standard forms always leads to a two level implementation

## Slide 33: 2 and 3 Level Implementation
Two Level Implementation
Three level implementation

## Slide 34: Digital Logic Gates (1/2)

## Slide 35: Digital Logic Gates (2/2)

## Slide 36: Positive and Negative Logic
The binary signal at the inputs and outputs of any gate has one of two values
One signal value represents logic 1 and the other logic 0
Since two signal values are assigned to two logic values, there exist two different assignments of signal level to logic value
Choosing the high‐level H to represent logic 1 defines a positive logic system
Choosing the low‐level L to represent logic 1 defines a negative logic system

## Slide 37: Integrated Circuits (1/4)
An integrated circuit (IC) is fabricated on a die of a silicon semiconductor crystal, called a chip, containing the electronic components for constructing digital gates
The various gates are interconnected inside the chip to form the required circuit
The number of pins may range from 3 on a small IC package to several thousand on a larger package
Each IC has a numeric designation printed on the surface of the package for identification

## Slide 38: Integrated Circuits (2/4)
Level of Integration
  Small Scale Integration (SSI)
    The number of gates is usually fewer than 10
    AND, OR, XOR etc ICs
  Medium Scale Integration (MSI)
    Have a complexity of approximately 10 to 1,000 gates in a single package
    Decoders, adders, and multiplexers
  Large Scale Integration (LSI)
    These devices contain thousands of gates in a single package.
    They include digital systems such as processors, memory chips, and programmable logic devices
  Very Large Scale Integration (VLSI)
    Contain millions of gates within a single package
    Examples are large memory arrays and complex microcomputer chips

## Slide 39: Integrated Circuits (3/4)
Digital Logic Families
  The circuit technology of an IC is referred to as a digital logic family
  TTL (transistor-transistor logic)
    50 years old and standard method
  ECL (emitter coupled logic)
    For high speed operations
  MOS (metal oxide semiconductor)
    Suitable for circuits that need high component density
  CMOS (complementary metal‐oxide semiconductor)
    CMOS is preferable in systems requiring low power consumption

## Slide 40: Integrated Circuits (4/4)
Fan‐out
  It specifies the number of standard loads that the output of a typical gate can drive without impairing its normal operation
Fan‐in
  It is the number of inputs available in a gate
Power dissipation
  It is the power consumed by the gate that must be available from the power supply
Propagation delay
  It is the average transition delay time for a signal to propagate from input to output
Noise margin
  It is the maximum external noise voltage added to an input signal that does not cause an undesirable change in the circuit output

## Slide 41: Quiz 1
Solution

## Slide 42: Quiz 1 (Paper A)
Question Number 1 [8 Marks]
Convert (124.43)5 to its binary equivalent

## Slide 43: Quiz 1 (Paper A)
Question Number 2 [1 + 5 + 1 + 3 + 2 = 12 Marks]
Two decimal numbers are given as A = 387 and B = 189.
  Write their equivalent BCD codes
  Add both these numbers by using BCD codes
  Convert A and B in base 6.
  Add them in base 6
  And prove that the answer is same as in decimal

## Slide 44: Quiz 1 (Paper B)
Question Number 1 [2 + 8 + 2 = 12 Marks]
Let A = 24, B = –12 and C = 38
  Represent them in 2’s complement form in binary by using 8 bits
  Calculate A – B – C by using 2’s complement method
  And verify that your answer is correct.

## Slide 45: Quiz 1 (Paper B)
Question Number 2 [4 x 2 = 8 Marks]
The state of a 12‐bit register is 100010010111. What is its content if it represents
  Three decimal digits in BCD
  Three decimal digits in the excess‐3 code
  Three decimal digits in the 6,3,1,1 code
  A binary number